# ChatOS Protocol : Anonymized direct TCP chat service

Abstract
This note describes the ChatOs Protocol (COP), a protocol used in ChatOS Application to route messages in TCP. COP can provides private connexion between two users or a public connexion to send messages for all users.

Summary
The ChatOs protocol is a very simple protocol used to communicate with other users. This document describes the protocol and its types of packets. The document also explains the reasons behind some of the design decisions.

# Purpose
The ChatOs Protocol is intended to be used for the
transmission of messages between clients. It may also be used for
the local message system of a network or host.

The focus here is on the internal mechanisms to transmit messages,
rather than the external interface to users. These will be both new
programs designed to work with this system and old programs designed
to work with earlier systems.

# Overview of the protocol

## Clients
A client is defined in the eyes of the server by a nickname and an IP address. The nickname is chosen by the user during his first connection, it must not be larger than the maximum size imposed by the server and must not be offensive or rude. Each user has his own nickname and must therefore be unique for better identification.

## Client identification
Clients are subject to a level of identification. An nickname lookup (and reverse check on this) is performed for all connections made to the server in order to avoid collisions with other nicknames which can lead to identification difficulties. Users are currently not subjected to a password check. Even if these checks are possible on all connections although the password check is currently not being set by the protocol.

## Message
Server and clients send each other messages wich may or may not generate a reply.
When a server receive a message, it MUST identify its source using (eventually assumed) nickname. If the nickname cannot be found in the server’s internal database, it then is registered if it is valid [See section 2.2]
ChatOs messages are always lines of characters and these messages SHALL NOT exceed 512 characters in length. There is no provision for continuation message lines.

## One-to-one communication
Communication on a one-to-one basis is usually only performed by clients. To send a private message you have to choose to whom to send the message. In order to provide a secure means for clients to talk to each other, it is required that the server is able to send a message in exactly one direction in order to reach any client.
Example : A message between clients 1 and 2 is only seen by server A, which sends it straight to client 2.
With this way, this provide a secure manner of exchanging messages with another client.

## One-to-all
The one-to-all type of message is better described as a broadcast message, sent to all clients. On a large network of users, a single message can result in a lot of traffic being sent over the network in an effort to reach all of the desired destinations.

## 2.6. Private connection
The establishment of a private connection between 2 users is achieved	by creating a TCP bridge relayed by the server between 2 clients to	guarantee permanent anonymity. Through this feature it is possible to	exchange messages for the moment.

## 2.7. Client commands
all the below-mentioned commands are automatically parsed at each new	instance
   if the command does not start with / or @, it is interpreted as a	public message.
   if the command is of the form @login message, the rest of the command	is interpreted as a private message for the login user.
   if the command is of the form /login file, the client will make a	private connection request for the login client if this connection	has not already been established. Once the connection is established,	the same command followed by a message will go throught the private	connection directly to the receiver.
Note: The commands available to clients depend on the context they	are in to avoid sending packets that are inconsistent with the	client's state.
For example, a client cannot select the option to send a public	message without being connected to the server first

# Implementation details

## Data representation:
Integers (Int) are 4 signed bytes and Bytes (Byte) represents bytes.	Strings (String) are encoded in UTF-8 and preceded by the size of	their representation in bytes on an Int in every packets which are	all transmitted in BigEndian.

## Introduction
To ensure the anonymity of each clients, the server redirects the messages provide by the sender with it’s own connection to the receiver.
## OP packet
| OP Code | Description |
+-----------|-------------------------------------------+
| 0 | Connection request with the server |
| 1 | Connection acceptance |
| 2 | Connection refusal |
   | 3 | Connection request with a specific user |
   | 4 | Public message |
   | 5 | Private message |
| 6	| Unknown user	|
| 7	| Private connection acceptance	|
| 8	| Private connection refusal |
| 9	| Unique Connect ID creation |
| 10	| Connect ID transmition |
| 11	| Private connection established |
   +-------------------------------------------------------+

## Identification
In ChatOS the first step for an user is to start a connection with the server. The user send a packet with the OPCode 0:

        Byte Int String
        +-------+-------------------+--------------+
        | 0 | nickname_size | nickname |

If the nickname is already use by an other user or it’s does
not respect the rules (too long, prohibited characters),
the server does not allowed the connection and send a connection	refusal packet.

  Byte Int String
        +-------+-----------------+------------+
        | 2 | sender_size | sender |

However, if the server accept then it send a connection acceptance packet indicating the client that he is free to come and now connected.

Byte Int String

+-------+-----------------+------------+
        | 1 | sender_size | sender |

## Private connection with an other client
The ChatOS specificity is to have establish a private connection between two users.
For this, the client will first ask the other client and send a private connection request packet through the server which will send it to the other client after that:
    Byte Int String Int String
+---+-------------+--------------+-------------+----------------+
   | 3 | S_nick_size | sender login | R_nick_size | receiver login |

If it’s a negative response, the client send back a connection	refusal packet to the server which is responsible to transmit it to	the sender client.

Byte Int String Int String
+---+-------------+--------------+-------------+----------------+
   | 8 | S_nick_size | sender login | R_nick_size | receiver login |

However if the response is positive then the receiver client send a connection acceptance packet to the server who transmit this packet to the sender client.

    Byte Int String Int String
+---+-------------+--------------+-------------+----------------+
   | 7 | S_nick_size | sender login | R_nick_size | receiver login |

If the user cannot be found by the server then the user receives a	packet with OpCode 6 from the server indicating that the recipient	cannot be found

Byte Int String
        +-------+-----------------+------------+
        | 6 | sender_size | sender |

The server then creates a unique id needed to establish the private connection which is communicated to both clients

 Byte Int String Int String Long
+---+-------------+--------------+-------------+----------------+----+
| 9 | S_nick_size | sender login | R_nick_size | receiver login | id |

Both clients can establish a private connection by connecting to the server with a new TCP connection each, over which they start by sending a packet containing the connect id obtained when the private connection was negotiated.

Byte Long
        +-------+------------------+
        | 10 | connect id |

When the server has accepted two TCP connections that have the same connect_id, it sends an aknowledgement packet command on both connections to each of the clients.

Byte
        +---------+
        | 11 |

From this point on, the private connection is considered established, clients can now communicate on this new private connection.

## Send a public message
When a client is connected into ChatOs, he can send a message for all connected users.
The client send a packet with the OP code 6 and his message coded in UTF8 charset:
 Byte Int String Int String
+---+-------------+--------------+--------------+---------+
| 4 | S_nick_size | sender login | message size | message |

Then the server broadcast it for each connected users.
Finally the clients catch and decode it to have the message and the sender’s nickname.

## Send a private message
To send a private message, an user need to be connected on the server and be aware of the other user's nickname. If it have these two conditions, the client can send a private message on the private connection with the code 4. (For more detailed description, refer to the section 2.4 One-to-One communication)

 Byte Int String Int String Int String
+---+------------+-----+------------+----------+--------+---------+
| 5 | exp_l_size | exp | rcv_l_size | receiver | m_size | message |

The server at the reception of the packet checks if the recipient's login is correct, if this is the case it sends the packet to the recipient afterwards.

If the user cannot be found by the server then the user receives a	packet with OpCode 6 from the server indicating that the recipient	cannot be found

Byte Int String
        +-------+-----------------+------------+
        | 6 | sender_size | sender |
# Normal Termination
The client is responsible for the termination. When a client want to end the connection with ChatOs server, it close all the connections which it is involved. That implies, the public connection and all privates connections. The others clients having a connection with him will be notified of his departure.

# Premature Termination
A premature termination will be occurred in some cases:
- When a client send a message or a file request without authentication with the server. In this case, the server send an ERROR packet and the TCP connection is closed.
- When a client has been inactive for more than 5 minutes he is disconnected. The others clients having a connection with this client will be notified of his departure. The server send an ERROR packet and the TCP connection is closed.
# Known concerns

## identification

Since the lifetime of a pseudonym for the client depends on the duration of its connection to the server, it is easy once the connection is closed to usurp the pseudonym by connecting from a new address but with the same name.

From the server's point of view, the client will not be the same because the name/address:port association is different, but as some of this information is hidden from other clients, they will only have access to the usurper's nickname and will not be able to tell the difference.

To overcome this problem, we would have to implement an SSL/TLS handshake protocol, but the goal of the chatOs protocol is to be simple to implement, which is why we do not use this type of security protocol.